SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Bayview Village Park

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM4505P |  | -improper spacing | -remove one swing and adjust |  | 2 |  |  |
| 3 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -entrapments | -modify | 20 | 2 |  |  |
|  |  | -non sufficient safety zone | -remove curb, reform | 2000 |  |  |  |
| PLG02TRM4505P |  | -play area | -cap beams | 100 | 4 |  |  |
| 2 Track Ride |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG03CHB4505P |  | -S-hooks | -replace | 10 | 1 |  |  |
| Hand to Hand Bars |  |  |  |  |  |  |  |
| PLG04SPR4505P |  | -none |  |  |  |  |  |
| Spring Toy - Duck |  |  |  |  |  |  |  |
| PLG05SPR4505P |  | -none |  |  |  |  |  |
| Spring Toy - Horse |  |  |  |  |  |  |  |
| PLG06SBW4505P |  | -none |  |  |  |  |  |
| Sand Box |  |  |  |  |  |  |  |
| PLG07JRW4505P |  | -barriers | -picket heights >30” with proper access / egress | 100 | 8 |  |  |
| Jr. Cr. Structure |  | -beams | -modify to less then 2” router |  | 8 |  |  |
| PLG07JRW4505P |  | -non sufficient safety zone | remove curb, reform | 2000 |  |  |  |
| con’t |  |  |  |  |  |  |  |
| PLG08SSM4505P |  | -none |  |  |  |  |  |
| Baby / Infant |  |  |  |  |  |  |  |
| PLG09INW4505P |  | -ramp goes to sidewalk | -take out ramp or add rubber surface | 1200 | 6 |  | T.B.A. |
| Handicap Int |  | -barriers | -picket egress/access over 48” | 100 | 6 |  |  |
|  |  | -beams | -modify to <2’ router |  | 6 |  |  |
|  |  | -steering wheel | -relocate |  | 1 |  |  |
|  |  | -pinch crush shear | -modify chain from bottom & router | 50 | 6 |  |  |
|  |  | -non sufficient safety zone | -remove curb, reform | 1000 |  |  |  |
| PLG01SRW4505P |  | -barriers | -picket and rail egress / access | 40 | 4 |  |  |
|  |  | -beams | -modify to <2’ |  | 4 |  |  |
|  |  | -non sufficient safety zone | -remove curb, reform | 1000 |  |  |  |
| Base Material |  | -compacted | -rototill, add base 80T |  | 8 | 1200 |  |
|  |  |  | -excavate |  | 8 | 1500 |  |
| Total |  |  |  | 7640 | 76 | 2700 |  |

File Name: K:\PLAY\NORTH\WARD-12\BAYVIEWV