SITE SPECIFIC RECOMMENDATIONS

EAST REGION:	Central District

LOCATION		Churchill Heights 														Ward 16

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 049 |  | - spacing | -adjust |  | 1 |  |  |
| 4 Baby |  | - improper seats | -replace | 200 | 1 |  |  |
|  |  | - hanger bearings | -invert bolts |  | 1 |  |  |
|  |  | - S-hooks | -replace | 10 | 1 |  |  |
|  |  | - safety zone | -excavate |  |  |  |  |
| PLG02SSM - 049 |  | - too many seats | -remove 2 and space |  | 1 |  |  |
| 6 Belt |  | - hanger bearings | -replace | 160 | 2 |  |  |
|  |  | - S-hooks | -replace | 10 | 1 |  |  |
|  |  | - safety zone | -excavate |  |  |  |  |
| PLG03TTM - 049 |  | - too many see-saws (< 48”) | -remove two |  | 2 |  |  |
| Quad See Saw |  | - cushioning | -add rubber to bottom of seats | 100 | 2 |  |  |
|  |  | - safety zone | -excavate |  |  |  |  |
| PLG04SST - 049 |  | - improper sides <4” | -replace sides | 200 | 4 |  |  |
| Jr. Structure Slide |  | - entanglement | -weld pieces | 50 | 2 |  |  |
|  |  | - barriers | -picket >30” | 200 | 2 |  |  |
|  |  | - safety zone | - excavate |  |  |  |  |
| PLG05TCM - 049 |  | - entanglement | -weld skirts | 100 | 2 |  |  |
| Tank Climber |  | - entrapment | - add pickets & straighten bars | 50 | 2 |  |  |
|  |  | - safety zone | - excavate |  |  |  |  |
| Base Material |  |  | -rototill, add base 22T |  | 8 | 660 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| TOTAL COST |  |  |  | 1080 | 40 | 1660 |  |

File Name: K:\PLAY\SCARB\WARD-16\CHURCHHI.WPD