SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	West District

LOCATION		Dovercourt Park														Ward 21

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -adjust bearings |  | 4 |  |  |
| 6 Belts |  |  |  |  |  |  |  |
| PLG02SSM |  | -nil |  |  |  |  |  |
| 2 Baby |  |  |  |  |  |  |  |
| PLG-03BAL |  | -nil |  |  |  |  |  |
| Balance Beam |  |  |  |  |  |  |  |
| PLG04TTM |  | -nil |  |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG05SPR |  | -nil |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG06INM |  | -entrapment (barrier & bridge) | -fill with wood | 10 | 4 |  |  |
| Sr. Cr. Structure |  | -access opening too wide | -install pickets | 150 | 15 |  |  |
|  |  | -fire pole too far from platform | -re-set | 10 | 4 |  |  |
|  |  | -tops of 6X6 | -cut 26 |  | 5 |  |  |
|  |  | -barrier on second bridge | -replace 14’ of barriers | 150 | 16 |  |  |
| PLG07INM |  | -swing attached | -remove |  | 6 |  |  |
| Jr. Cr. Structure |  | -no barriers around platform | -add 25’ lineal | 200 | 16 |  |  |
|  |  | -head entrapment on roof | -remove |  | 6 |  |  |
|  |  | -entrapment in stairs | -fill with wood |  |  |  |  |
|  |  | -steering wheel | -replace with solid one | 60 | 1 |  |  |
|  |  | -improper sides on slide | -replace | 2000 | 10 |  |  |
|  |  | -6X6 tops | -cut on angle |  | 4 |  |  |
| Base Material |  | -compacted | -rototill, add base material 1T |  | 8 | 15 |  |
|  |  |  | -excavate |  | 8 |  |  |
| TOTAL COST |  |  |  | 2580 | 107 | 15 |  |

File Name: K:\PLAY\SOUTH\WARD-21\DOVERCRT.WPD