SITE SPECIFIC RECOMMENDATIONS

WEST	REGION:	West District

LOCATION		Florence Gell Park														Ward 27

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove two swing, adjust spacing |  | 1 |  |  |
| 6 Belt |  | -play surface on top of frame | -install angled wood | 100 | 4 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -non encroachment zone | -remove one bay, relocate other |  | 8 |  |  |
| PLG02SSM |  | -S-hooks | -replace | 10 | 1 |  |  |
| 3 Baby |  | -improper spacing | -remove one, adjust spacing |  | 1 |  |  |
|  |  | -play surface on top of frame | -install angled wood | 100 | 4 |  |  |
|  |  | -non encroachment zone | -relocate |  | 8 |  |  |
| PLG03SRM |  | -play surface on all top rails | -install 1” strip on top | 200 | 4 |  |  |
| Sr. Cr. Structure |  | -play surface on all head posts | -install caps | 100 | 2 |  |  |
| PLG04JRM |  | -play surface on all top rails | -install 1” strip on top | 200 | 4 |  |  |
| Jr. Cr. Structure |  | -play surface on head post | -install caps | 100 | 2 |  |  |
| PLG05SPR |  | -nil |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill, add base material 4T |  | 8 | 60 |  |
|  |  | -non sufficient safety zone | -excavate |  | 16 | 1000 |  |
| TOTAL COST |  |  |  | 820 | 64 | 1060 |  |

File Name: K:\PLAY\ETOBI\SOUTH\WARD27\FLORENCE