SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Harryetta Gardens	         													Ward 8

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM2553P |  | -improper spacing | -replace bearings | 200 | 8 |  |  |
| Swing Set |  |  |  |  |  |  |  |
| PLG02SSM2549P |  | -improper spacing | -replace top rail | 200 | 6 |  |  |
| Swing Set |  |  |  |  |  |  |  |
| PLG03TTW2549P |  | -none |  |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG04SPR2549P |  | -none |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG05SPR2549P |  | -none |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG06CAR2549P |  | -none |  |  |  |  |  |
| Playshell |  |  |  |  |  |  |  |
| PLG07JRW2549P |  | -horizontal pickets | -change to vertical | 200 | 3 |  |  |
| Jr. Cr. Structure |  | -no grips at access | -install grips | 100 | 6 |  |  |
|  |  | -elevated play surfaces | -cap | 50 | 6 |  |  |
| PLG08SRW2549P |  | -improper railing on bridge | -picket bridge | 200 | 8 |  |  |
| Sr. Cr. Structure |  | -transition at bridge | -picket access | 200 | 2 |  |  |
|  |  | -low railing around sr platform | -raise and replace one piece blue plastic | 200 | 8 |  | -one piece 4’X8’ staywhite |
|  |  | -entanglement at Jr straight slide | -picket entrance | 100 | 2 |  |  |
|  |  | -access to fire pole & rope climber too big | -picket access | 50 | 4 |  |  |
|  |  | -fire pole not 60” from platform | -remove |  | 2 |  |  |
|  |  | -no hand grips at access | -install grips | 100 | 10 |  |  |
|  |  | -hole in tube entrance | -replace | 300 | 6 |  |  |
|  |  | -hole in bubble | -replace | 250 | 3 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 | 600 |  |
|  |  | -200 feet of 6 X 6 edge two deep | -excavate |  | 16 | 1000 |  |
| Total |  |  |  | 2150 | 98 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-8\HARRYETT