SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Huron - Washington														Ward 24

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one seat, adjust spacing |  | 2 |  |  |
| 3 Belt |  | -fence in 2Y zone | -relocate swing 2’ south | 20 | 20 |  |  |
| PLG02SSM |  | -tree in 2Y zone | -remove swing set |  | 10 |  |  |
| 3 Belt, 3 Baby |  |  |  |  |  |  |  |
| PLG03SSM |  | -improper spacing | -remove two, adjust spacing |  | 2 |  |  |
| 4 Baby |  |  |  |  |  |  |  |
| PLG04SPR |  | -protrusion on handle & footrest | -remove and replace | 1200 | 4 |  |  |
| Duck Spring Toy |  |  |  |  |  |  |  |
| PLG05SPR |  | -entrapment between seat & footrest | -fill with wood | 10 | 1 |  |  |
| Elephant Spring Toy |  |  |  |  |  |  |  |
| PLG06INM |  | -entanglement on slide | -caulk gap | 10 | 1 |  |  |
| Hill & Dale |  |  |  |  |  |  |  |
| PLG07JRM |  | -improper barriers | -picket 4: | 35 | 3 |  |  |
| Jr. Cr. Structure |  | -window holes too big | -cover with plexi glass | 100 | 2 |  |  |
|  |  | -climbable roof | -cover with plastic | 1000 | 2 |  |  |
| PLG08SRM |  | -improper barriers | -picket 50’ | 400 | 40 |  |  |
| Sr. Cr. Structure |  | -open steering wheel | -replace with solid | 60 | 1 |  |  |
|  |  | -entrapment in rope climber | -remove and replace | 250 | 8 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| TOTAL COST |  |  |  | 3085 | 104 | 0 |  |

File Name: K:\SOUTH\WARD-24\HUR-WASH.WPD