SITE SPECIFIC RECOMMENDATIONS

WEST	REGION:	East District

LOCATION		Nairn Park															Ward 28

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one swing, adjust spacing |  | 1 |  |  |
| 3 Belt |  | -S-hook | -replace | 10 | 1 |  |  |
|  |  | -hanging bearings | -replace | 50 | 2 |  |  |
| PLG02SSM |  | -S-hooks | -replace | 10 | 1 |  |  |
| 2 Baby |  | -play surface on top frame | -install angled wood | 50 | 2 |  |  |
| PLG03SRM |  | -tire swing not up to standard | -remove |  | 2 |  |  |
| Sr. Cr. Structure |  | -play surface on all top rails | -install 1” strip | 200 | 4 |  |  |
|  |  | -play surface on all head posts | -install caps | 100 | 4 |  |  |
|  |  | -monkey bars not up to standard | -remove |  | 2 |  |  |
|  |  | ->15” opening for fire man pole | -install pickets | 25 | 1 |  |  |
|  |  | -barriers required on platform | -install pickets | 100 | 2 |  |  |
|  |  | -entrapment between platform | -install plywood | 100 | 2 |  |  |
| PLG04JRM |  | -play surface on top rails | -install 1” strip | 200 | 4 |  |  |
| Jr Cr. Structure |  | -play surface on head post | -install caps | 100 | 4 |  |  |
|  |  | -pickets on barriers & stairs | -install pickets (20) | 250 | 6 |  |  |
|  |  | -entrapment between platforms | -install plywood | 100 | 2 |  |  |
| Base Material |  | -compacted | -rototill, add base 8T |  | 8 | 120 |  |
| TOTAL COST |  |  |  | 1295 | 48 | 120 |  |

File Name: K:\PLAY\ETOBI\WARD-28\NAIRN.WPD