SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Old Sheppard Park														Ward 12

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PL601SSM4564P |  | -non sufficient safety zone | -cut supports & chains down to intermediate - reduce height | 100 | 8 |  |  |
| 2 Belt Senior |  | -S-hooks | -replace | 10 | 1 |  |  |
| PL602SSM4564P |  | -S-hooks | -replace | 10 | 1 |  |  |
| 2 Baby |  | -play area | -modify beam | 50 | 2 |  |  |
| PL603INW456P |  |  |  |  |  |  |  |
| Int/Jr Creative Structure |  | -play surface greater than 2” | -replace 4X4 divider with 2X6 on int/jr | 75 | 4 |  |  |
|  |  | -entanglement | -modify slides | 20 | 2 |  |  |
|  |  | -barriers | -extend to 3” from slide & platforms | 600 | 6 |  |  |
| PL604SSP4564P |  | -entrapment | -add backing to stairs | 300 | 6 |  |  |
|  |  | -barriers | -extend down to platform or modify | 150 | 3 |  |  |
| PL605TRH4564P |  | -none |  |  |  |  |  |
| Triple Hoop |  |  |  |  |  |  |  |
| Base Material |  |  | -rototill |  | 8 |  |  |
|  |  |  | -add base 80 T |  |  | 1500 |  |
|  |  |  | -excavate |  | 8 | 1200 |  |
| Total |  |  |  | 1315 | 49 | 2700 |  |

File Name: K:\PLAY\NORTH\WARD-12\OLDSHEPP