SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Prince Charles Park        													Ward 8

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM2552P |  | -play surface on top rail | -cap | 50 | 2 |  |  |
| Swings |  |  |  |  |  |  |  |
| PLG0SPR2552P |  | -protrusions | -remove |  | 2 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG03BAD2552P |  | -non sufficient safety zone | -relocate | 25 | 4 |  |  |
| Backhoe Digger |  |  |  |  |  |  |  |
| PLG04STS2552P |  | -no clearance | -replace top bar to increase clearance | 200 | 16 |  |  |
| Tire Swing |  | -too heavy | -replace with lighter tire | 100 | 4 |  |  |
| PLG05JRW2552P |  | -play surfaces | -cap | 20 | 2 |  |  |
| Jr. Cr. Structure |  |  |  |  |  |  |  |
| PLG06SRW2552P |  | -entrapment on open steering wheel | -replace steering wheel | 60 | 1 |  |  |
| Sr. Cr. Structure |  | -track ride attached & in spiral slide zone | -remove |  | 2 |  | -room to relocate |
|  |  | -transitions from jr. to sr. | -picket transition | 300 | 3 |  |  |
|  |  | -open barriers | -replace | 500 | 6 |  |  |
| PLG07SBW2552P |  | -none |  |  |  |  |  |
| Sand Box |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
| Total |  |  |  | 1255 | 50 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-8\PRINCECH.WPD