SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	East York District

LOCATION		George Webster														Ward 1

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 4 Baby |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -encroachment | -remove wood border |  | 4 |  |  |
| PLG02SSM |  | -improper spacing | -remove three, adjust spacing |  | 1 |  |  |
| 6 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -encroachment | -remove wood border |  | 4 |  |  |
| PLG03SRM |  | -barriers | -picket > 48” | 600 | 6 |  |  |
| Sr. Cr. Structure |  | -fireman pole | -replace | 100 | 2 |  |  |
|  |  | -play area | -cap supports & beams | 300 | 4 |  |  |
|  |  | -encroachment | -remove wood border |  | 4 |  |  |
| PLG04SSP |  | -barriers | -add pickets | 300 | 4 |  |  |
| Sr. Spiral Slide |  | -slide exit | -add 12 < 5º | 400 | 4 |  |  |
| PLG05SSM |  | -tire | -remove and add two baby swings | 200 | 2 |  |  |
| Tire Swing |  |  |  |  |  |  |  |
| Base Material |  | -non sufficient safety zone | -excavate |  | 8 | 1500 |  |
|  |  |  | -add base material 88T |  | 8 | 1320 |  |
| Total Cost |  |  |  | 1920 | 54 | 2820 |  |

File Name: K:\SCARB\WARD-1\WEBSTER