SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Willesden Park														Ward 12

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM4595P |  | -non sufficient safety zone | -excavate and add base material |  |  |  |  |
| Senior 4 Belt |  | -support bars heaved, cement showing | -re-set | 100 | 8 |  |  |
| PLG02SSM4595P |  | -middle post heaved, cement showing | -re-set to proper depth | 100 | 8 |  |  |
| Int 4 Belt |  | -non sufficient safety zone | -excavate and add base material |  |  |  |  |
|  |  | -top beam bent | -replace | 50 |  |  |  |
| PLG03SSM4595P |  | -improper spacing | -remove one swing and adjust |  | 3 |  |  |
| Jr 3 Baby |  | -non sufficient safety zone | -excavate and add base material |  |  |  |  |
|  |  | -support bars heaved, cement showing | -re-set | 100 | 8 |  |  |
| PLG04CRC4595P |  | -non sufficient safety zone | -excavate and add base material |  |  |  |  |
| Rocket Climber |  | -entrapment, crush & shear points | -modify | 200 | 6 |  |  |
| PLG05SST4595P |  | -improper barriers | -remove and replace with senior slide | 2000 | 8 |  |  |
| Int Sr. Slide |  | -support heaved, cement showing |  |  |  |  | -metal |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -base 160T |  |  | 2400 |  |
|  |  |  | -excavate |  | 8 | 2500 |  |
| Total |  |  |  | 2550 | 57 | 4900 |  |

File Name: K:\PLAY\NORTH\WARD-12\WILLESDEN