SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Garden Avenue														Ward

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 074 |  | -improper spacing | -remove two baby, one belt |  | 1 |  |  |
| 4 Baby, 2 Belt |  | -hanger bearings | -replace | 120 | 2 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG02SST - 074 |  | -entrapment | -remove and replace | 1200 | 8 |  |  |
| Jr. Str. Slide |  | -entanglement |  |  |  |  |  |
| PLG03TTM - 074 |  | -improper spacing | -remove two, adjust |  | 2 |  |  |
| Quad Teeter Totter |  | -cushioning | -add rubber to bottom of seats | 150 | 3 |  |  |
| PLG04TCM - 074 |  | -entrapment | -weld shut | 50 | 2 |  |  |
|  |  | -entrapment | -modify bars |  | 2 |  |  |
| Base Material |  | -compacted | -rototill, add base material 88T |  | 8 | 1320 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1500 |  |
| Total Cost |  |  |  | 1530 | 37 | 2820 |  |

File Name: K:\PLAY\SCARB\NORTH\GARDENAV