SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Windfields Park															Ward 9

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW5012P |  | -elevated play surface | -cap |  |  |  | -site replacement |
| 4 Belt Swing Set |  | - |  |  |  |  |  |
| PLG0201SSW5012P |  | -not up to standard | -remove |  |  |  |  |
| 1 Tire Swing Set |  |  |  |  |  |  |  |
| PLG0301SSW5012P |  | -elevated play surface | -cap |  |  |  |  |
| 6 Baby, 2 Belt |  | -improper spacing | -remove swings and adjust |  |  |  |  |
|  |  | -seats | -new baby seats |  |  |  |  |
| PLG04SPR5012P |  | -protrusions | -retrofit or replace |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG05SPR5012P |  | -protrusions | -retrofit or replace |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG0601JRW5012P |  | -need pickets | -add pickets |  |  |  |  |
| Jr. Cr. Structure |  | -shear points on steering wheel | -replace wheel |  |  |  |  |
|  |  | -entanglement - no sidewall | -in-fill and retrofit |  |  |  |  |
|  |  | -rope on ramp pinch pts | -remove rope |  |  |  |  |
|  |  | -insufficient safety zone | -remove lockstone |  |  |  |  |
| PLG0701INW5012P |  | -climber ladder | -remove first rung |  |  |  |  |
| Int. Cr. Structure |  | -timber bridge | -close in bottom |  |  |  |  |
|  |  | -track ride | -safety zone |  |  |  |  |
|  |  | -tube slide | -remove & replace |  |  |  |  |
|  |  | -barriers insufficient | -replace or add in fill |  |  |  |  |
|  |  | -access ladder spacing size | -change to standard |  |  |  |  |
|  |  | -rope climber | -retrofit and change hardware |  |  |  |  |
|  |  | fire man pole attached | -in fill |  |  |  |  |
| Sand Box |  | -elevated play surface | -relocate |  |  |  |  |
| Tic-Tac-Toe |  | -elevated play surface | -relocate |  |  |  |  |
| Base Material |  | -compacted | -rototill |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
|  |  |  | -base material 80 T |  |  |  |  |
| Total |  |  |  | 0 | 0 | 0 |  |

File Name: TGRENCI\CORELWP\JAMIE\SESITEIN\WINFIELD